## Slide 1: changelog
10/18/2018 tte – initial slides

## Slide 2: BIER in ROLL Design Team
Consider joining/collaborating in BIER design team in ROLL-WG:
Email: roll-bier-dt@ietf.org (normal subscribe)
Issues: tte@cs.fau.de
What could be cool about this (if design team decides to do it) ?
End-to-end BIER (with TE) in low-power networks (e.g.: building control)
  Example: Application Controller sends BIER packet to subset of clients (lightbulbs)
  Each client is BFER (has a bit)
  Every packet can address a separate subset of actors through bitstring
  Only controller app needs to be BIER aware. Receivers can think its just IP multicast.
BIER TE bits to save power/memory
  Routers are low-power (memory/CPU). Do not want to keep large routing table (1000 lightbulbs). Links are low power too.
  Every interface has a bit. Routers only need to route on bits to directly connected downstream neighbors.
No ASIC constraints. Everything is software
  Headers/Bitstring can be compressed (loss free, lossy (bloom) to support long bitstrings.
  Should result in header more compact than existing ROLL/RPL headers even for unicast: Only hop-by-hop bits sets to one receiver: Would also be used for unicast forwarding.
ROLL/BFER
stack
IP multicast App
10..1000 clients/actors
ROLL/BFR
Low-power
router
ROLL/BFIR
Root node
1
2
3
4
6
5
10
Bits for interfaces
(BIER-TE) to allow
explicit steering of
traffic
Root also acts as
Controller assigning/
Managing Bits
BIER aware
Application
Controller
Tunnel Encap
BIER / IP
App-Payload
Data Packet
Root node adds
Interface bits and
compresses header ?!
Application controller can efficiently send packets to
Every subset of receivers by being BIER aware.
AnyTransit
Slide v1.0
Control: learn which bit maps to which client
11.. 999

## Slide 3: Framework ROLL+BIER+6LowPan
Tunnel Mode
  BIER, BIER-TE: Bits assigned to 6LR
  BIER-TE: Bits also assigned to adjacencies/6TR
  No bits assigned to 6LN
Services
  BIER 6SN-> 6LR + BA
  IP unicast 6SN -> 6LR/6LN + IA
6LowPAN + BIER
  Compress/uncompress unicast/multicast packets
  6RR … 6LR
  6LR ... 6LN ???
6RR
1
2
3
4
6
5
10
Slide v1.0
11.. 2000
RPL + BIER routers
Roles:
6RR = root.
needs to support 6LowPanBIER
6TR = transit – no bit in BIER mode
6LR = leaf (LowPan) Router bit in BIER mode,
connects to 6LN
needs to support 6LowPanBIER
6LN = Lightweight Node
no knowledge of ROLL/BIER
only needs to support 6LowPan with BIER extensions
6SN = Server Node / Application
Not running ROLL/BIER
able to send packets with BIER bitstring to target set of destinations explicit
BA = BIER aware app able to send/rcv
packets with bitstring, no IP multicast needed IA = IP unicast/multicast app. No BIER awareness
6TR
6LR
6LR
6SN
6LN
6LN
6LN
6TR
6TR
Explanations
Topology

## Slide 4: 6LR diagram
Lookup Bitstring | Function
256 bits | Next-hop 6TR
256 bits | …
256 bits | Next-hop 6TR
256 bits | Punt (I am 6LR)
Bloom filter bitstring
Forwarding table(s)
6LowPan
6LowPan
BIER(-TE) forwarding
Storing mode (BIER):
#6LR entries
Non-storing mode (BIER):
#adjacent 6LR/6TR
+1 if we are 6LR
Bit | Function | Reset/FBM
1 | Next-hop 6TR | 256 bits
… | … | 256 bits
… | IGNORE | 256 bits
N (256) | Punt (I am 6LR) | 256 bits
Explicit bitstring Forwarding table(s)
Storing Mode
RPL routing table
6LR Bit to IPv6addr
mapping
One forwarding rule for bloom-filter, one for explicit bitstring. Distinction BIER/BIER-TE is just in how forwarding table gets populated
Only for storing-mode/BIER,
Not used with BIER-TE
Compress/Decompress packets on the wire (L2.5)
Calculate bloom filter,
populate
Populate
6RR
6LR
(Calculate bloom filter)
Populate forwarding tables on all 6LR
Only for non-storing-mode/BIER,
Not used with BIER

## Slide 5: TBD: IP multicast over ROLL-BIER
Show IP Multicast layer on 6RR / 6LR / 6LN

## Slide 6: Bloom Filter considerations (not reviewed)
With bloom filter bitstring, bits can not be reset
BIER logic
  Leads to duplicates. Other radio-network issues can also lead to duplicates, so maybe not a big issue – radio networks MUST be prepared to deal with duplicates
  Routing protocol microloops are avoided by reset. If RPL can have microloops they would only be protected against by TTL expiry (eg.: > 100 packet replications possible).
  False positives in bloom filter can create more duplicates and more replicated packet when there is a routing microloop
With BIER-TE
  No routing protocol involved = no IGP microloops.
  False positives can create duplicates AND looping (like badly set bits by BIER-TE controller can create loops too)
Solutions ?
  Have ROLL-BIER domain TTL (6LowPan TTL ?) that is set to be as small as possible: longest path to any receiver. Calculated by root node ?!
    With common network diameter < 8 ?! This should be good enough ?! (4 bits enough to encode ?)
  Duplicate elimination by packet-ID ? Probably takes too much memory…

## Slide 7: BIER consideration (not reviewed)
With bitstring length N, we need N * N bits for FBM – reset bits
  With bloom filters, we can not have FBM (reset bits). But we try to resolve that issue
  Do we want to forego FBM for non-bloom filter ?
  Less problems to solve than with bloom filter: No false positives! Just more duplicates, routing microloop duplicates.
Simple option ?
  Make FBM a “SHOULD” – low-end devices could optimiz them away.
Quantify benefit of explicit BIER bitstring (not BIER-TE)
  Unicast: Do we save anything over existing storing mode with 6LowPan ? (header already well compressed)
    Maybe there is NO reason to use BIER bitstring for unicast (only BIER-TE)
  Multicast: assume existing storing mode network (aka: overhead of unicast routes acceptable)
    BIER avoids to introduce another multicast routing protocol (PIM, RPL-multicast state,…)
    More efficient use of bits (no bits used for adjacencies, just 6LR

## Slide 8: BIER consideration (2, not reviewed)
Option position summary ? All need to be validated/quantified.
Non-storing mode networks
  Use BIER-TE == non-storing. Unicast+multicast.
  Can further minimize state avoiding FBM memory
  Smaller networks use explicit bitstring. Larger ones use bloom filter.
Networks with storing mode routers
  Use BIER, maybe just multicast. No benefit? to use for unicast.
  Smaller networks use explicit bitstrings, larger ones use bloom filter.

## Slide 9: Bitstring / BIER considerations
Explicit BIER-TE bitstring allows to save memory on 6TR/6LR:
  Do not need RPL routing entries for all 6TR/6LR.
With BIER, we do need RPL routing table for all 6TR/6LR
  What do we save (why BIER) ? Unclear / need to better caracterize.
  Comparison complex ? Because we also have to take savings from 6LowPan into account.
Aka: Do we need to consider Explicit Bitstring + BIER ?
  Forwarding plane can be the same BIER/BIER-TE. Eliminating BIER just reduces control plane work to consider (RPL -> create BIER forwarding table entries).
  BIER/BIER-TE forwarding more similar than outside of ROLL:

## Slide 10: Open
With BA (bier aware application) we could send non-IPv6 payload. Any benefit in that ?
  No ? 6LowPan would compress IP header away so there is no benefit eliminating IP ??
Unicast between 6LR/6LN ? Unicast 6LR/6LN towards 6RR ?
  How do we deal with that ?
IEF Multicast likes SSM.
  SSM could help to address 6SN (which server needs to know about IGMP memberships). Part of

## Slide 11: Refuse

## Slide 12: Refuse - Does not work
Does not work: Multicasting unicast packets
  Aka: unicast packet replicated via bitstring to more than one destination
  Could recreate packet with each destinations unicast dest-addr, but:
    No architecturally clean solution to do so – e.g.: UDP checksum calculation
  Make destination address a “unicast-group-address” – IPv4/IPv6 unicast address same on all nodes
    Avoid problems like UDP checksum
    But would just reinvent IP multicast service with IP unicast addresses (which we will have). No added value.
Slide v1.0

## Slide 13: Refuse - Below the line (now)
Using BIER to carry non-IPv6 packets
  Idea was: BIER packets can directly carry any payload, no IPv6-multicast heade required, eliminate overhead/complexity of IPv6
  Claim: 6LowPan can compress the IPv6 headers so much that there is not enoug initial value in designing header stacks to eliminate IPv6.
  But: We need to make sure 6LowPan will also equally well compresses the IPv6 multicast header
  Also eliminates need to figure out how to deal with false-positives for non-IPv6—multicast BIER packets
Below the line: Transport mode
  In transport mode, 6LN nodes will have bits assigned to them in the bitstring. This introduces the need for them to be more aware of BIER, e.g.: introduce more BIER awareness into 6LowPan+BIER
  For unicast
    Will work fine but below line until we have evidence that it could provide better compression than tunnel mode with 6LowPan+BIER compression.
  Transport mode for multicast
    Just too much work trying to figure out in first round how to build a lightweight node that ALSO has to be aware of BIER bitstrings.
Slide v1.0

## Slide 14: TO BE DISCUSSED

## Slide 15: IP Multicast layer

## Slide 16: IP Multicast layer overview
Primary target for IP Multicast in ROLL-BIER
  Efficient sending/replication of multicast packets from IP multicast sender (app) on 6SN to IP multicast receiver (app) on 6LN/6LR
  App on 6SN should be able to explicitly indicate set of receivers. Key benefit not possible with BIER not possible with standard IP multicast.
    Example from design-team slide: send “ON”/“OFF” message to subset ot light-bulbs that should be switched “ON”/”OFF”
Not needed: Send IP multicast packets from 6LR/6LN
    Application client/server mode:
    Application has one or more server (6SN) sending IP multicast through tunnel into 6RR. Clients (6LR/6LN) can just receive IP multicast.
    Client->client multicast “emulated” by client sending unicast to Server and then server sends IP multicast
      Client may receive its own IP multicast packet back, so application need to be able to recognize/filter packets from “itself”
      Client on 6LR can be excluded from bitstring by 6SN, so this additional filtering only required for 6LN
6RR
1
2
3
4
6
5
10
11.. 2000
6TR
6LR
6LR
6SN
6LN
6LN
6LN
6TR
6TR
BA = BIER aware app
IA = IP unicast/multicast app. No BIER awareness
Tunnel
6SN
6SN

## Slide 17: IP Multicast layer: SSM only
Majority of IETF Multicast experts prefer SSM IP Multicast over classical ASM IP Multicast
  Proposal follows that direction
  SSM: receivers send (S,G) membership instead of (G) membership (MLDv2).
  S = sender (Server) IP unicast address.
Benefits
  If we want to avoid implement directly client->client IP multicast in ROLL-BIER, we need Client/Server model, only servers allowed to send IP multicast, client unicasting to server if they need to be able to send IP multicast (previousslide). This is exactly the model how IP multicast would be done with SSM.
  SSM avoid need to coordinate IP multicast group addresses across applications (potentially big operational issue).
  When SSM IP multicast application on a sender wants to create a new SSM stream, it simply needs to allocate an SSM IP multicast group that is unused on this sender (like allocating an TCP port unused for a new unicast service).
  Client discovery of SSM (S,G) ? Use same scheme a for Unicast server discovery in the absence of IP multicast (e.g.: DNS). As necessary, extend discovery to also discover IP Multicast group (e.g.: Put Server IP unicast address and group-address into DNS. E.g.: group-address in TXT record).
  Ideal: New IP multicast application on 6SN can allocate new local IPv6 address (independent from IPv6 address used by other IP multicast app running on same 6SN)
    Benefit: Applications that can have their own SSM IP Multicast sender IPv6 addresses can use static/well-known IPv6 Multicast group application – no need for group discovery by receivers.
    Best method for local address allocation ? IPv6 privacy addresses ?... ?

## Slide 18: IP Multicast layer: MLDv2
Why do we even need MLDv2 ?
Not for 6LR: Receiver application on 6LR will receive multicast packet because of bit in BIER bitstring. No IGMP/IP Multicast needed.
Receiver on 6LN will receive link-layer multicast packet across access-subnet with potentially many 6LN.
  (S,G) IP multicast header indicates whether packet is of interest to receiver
  6LR needs to know whether to send packet to a particular subnet. Some signaling needed to learn this from receivers. No need to reinvent wheel: MLDv2 does this.
  Receivers need to open link-layer filter (eg: destination) to receive multicast and send packets up to right application. OS-level MLDv2/multicast-socket-API does this. No need to reinvent the wheel.
BUT!! Above reasoning to reuse/not-modify 6LR->6LN IP multicast (SSM) is ONLY true if IP Multicast packet actually contains IPv6 Multicast header.
  If we want compressed packet on 6LR->6LN link, then the above rules may not be true: If new OS-level code is needed on 6LR/6LN to support 6LowPan compressed IP multicast packets, then we should re-evaluate what the most pragmatic way is to get a working solution.
  Unclear what exists today wrt. 6LowPan/IP-multicast/compressed-packets.

## Slide 19: IP Multicast layer: proposal (1) - INCOMPLETE
6LN:
  Signaling: SSM subset of RFC3810 (MLDv2), host side
    Note: This should also be subset of “lightweight IGMPv3/MLDv2” (RFC5790)
  Only need to be able to receive, not send IP multicast
  6LowPan (extension?) to receive compressed IP multicast packets
6LR:
  Signaling: SSM subset of RFC3810 (MLDv2), router side
  (Modified/Extended) SSM subset of RFC4605 (IGMP/MLD proxy routing)
    6LR aggregates SSM receiver state from all subnets: 6LN + internal virtual subnet for IP Multicast receiver application on 6LR itself.
    6R sends aggregated membership state to 6SN (join/leave): HOW? (later slide)
    Any BIER packet with 6LR “bit” set or 6LR comb filter match will be passed to MLD proxy routing forwarding as coming ”from upstream”
    NO receiving of IP multicast packets from downstream nodes (6LR, 6LN) – just discard
6TR:
  Do not participate in P multicast layer. Just forward BIER. Become 6LR when BIER bitmask/comb-filter entry exists for them. Every 6LR is also always 6TR (forwards BIER independent of processing IP Multicast)
6RR:
  Just like 6TR except that it also must be able to receive tunneled IP Multicast + (pseudo) BIER header from 6SN.

## Slide 20: IP Multicast layer: issue
Simple: let 6SN “just” send SSM IP multicast. No BIER improvements
  Receipt of IP multicast ONLY determined by MLDv2 membership from receivers (6LN / 6LR).
  Foregoes application benefits of using BIER (sender determines receivers)
Problem: Can not get BIER benefit for 6LN without non-heuristic bitstring transport mode”
  Give BIER bits to 6LN, carry bitstring all the way to 6LN
  Can not use heuristic likely not useful here: need to be able to eliminate false positives at application level.
Design for ONLY SSM IP multicast different / simpler as if we want to introduce application layer BIER benefits to application

## Slide 21: IP Multicast ONLY model
6LR send aggregate MLD membership (join/leave) to RR.
6LR keeps (S,G) -> { 6LRi } state.
Keep table of Bits(6LRi) -> bitstring:
  bitstring with one bit (non-bloom, BIER)
  bitstring with > 1 bits (non-bloom, BIER-TE):
    BIER bit for 6LR plus bits for each hop towards it.
  bitstring with > 1 bits (bloom BIER/BIER-TE). Bloom compression bitstring result for 6LR (BIER) plus Bloom compression bitstring result for each hop towards it (BIER-TE).
6SN just send IP multicast to RR via some tunnel
  RR may perform RPF check (source address must be 6SN unicast address).
  Then encaps/forwards BIER/BIER-TE:
    Loop up (S,G) of packet, Ors Bits(6LRi) for all { 6LRi }. Sends packets
At minimum same type of hop-bits determination for BIER-TE / non-storing mode as used for unicast non-storing mode today. Just encoded as direct/bloom-filter bits.

## Slide 22: IP Multicast + 6SN BIER model
6SN should indicate set of destinations instead of “just” MLDv2 join state
As long as we assume we always use IPv6 multicast packet / MLD, the set of destinations indicated by 6SN must be subset of the “joiners”
  Simple app example: Each application just has ONE IPv6 multicast group, all application members on 6LR / 6LN join to that group. But 6SN only indicates subset of those application clients for each packet.
  Does not work for 6LN without transport mode (prior slide).
Most simple? Hybrid solution (introduce BIER benefit to 6SN with minimum additional work ?)
  RR forwards (S,G) -> { 6LR } state changes to 6SN. Use of SSN makes this easy: Each 6SN only gets updates for those (Si,G) with its own Si.
  6SN send IP Multicast packet with additional BIER pseudo-header
    Indicating subset of 6LR to which packet should go
  6RR then only OR’s bitstrings for this subset as opposed to full { 6LR } it maintains
INCOMPLETE

## Slide 23: Next steps ?!
Push discussion about BIER interface for 6SN to BIER-WG ?!
  ROLL should not come up with somethin ROLL specific that does not have to be ROLL specific – better try to find general purpose solution in BIER (ROLL defining requirements)
SSM IP multicast (ONLY) solution
  ROLL: (optional) ? compression for 6lowPan extension on access LAN
  “Tunnel” from 6SN node to 6RR - to send IP Multicast packets from 6SN to 6RR
    Two cases ?
    A) 6SN is inside 6LowPan network: simple 6LowPan header extension: one bit to indicate “packet goes to root”, but also encode IP Multicast Group address.
    B) 6SN is “behind backbone”: Need an actual IP tunnel (path between 6SN/6RR not natively supporting 6LowPan). Just encapsulate same 6LowPan packet inside ?
  MLDv2 proxy operations on 6LR
    6LR -> 6RR covered by ‘draft-ietf-bier-mld-01.txt’, but discovery of 6RR and constraints (only receive, not sending) and 6LR->6LN not covered.